## Slide 1: STM32 with Motor driver
01.11.2024
Student Lab 2b

## Slide 2
Lab2 content
Lab2a: Setting up hardware
- Connection of Motor driver board to NUCLEO board for driving Mirror’s motors
- Connection of 4 (four) buttons
Lab2b:
- Forward and reverse of motor using buttons (one button and four buttons)

## Slide 3
!! Before entering Lab 2b !!
The students must done Lab2a
All connection must be checked first by the Instructor

## Slide 4
Lab2b
Forward and reverse of motor using buttons
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 5: Lab2b: Forward and reverse of motor using buttons
In this lab, we will drive Mirror’s motors (2 motors) forward and reverse using one and four buttons
Driving Mirror’s motors forward and reverse using one button:
    First pressing  motor 1 runs in forward direction for 1s
    Second pressing  motor 1 runs in reverse direction for 1s
    Third pressing  motor 2 runs in forward direction for 1s
    Fourth pressing  motor 2 runs in reverse direction for 1s
    Another pressing will come back to first pressing, and so on
    No button is pressed  no motor running
Driving Mirror’s motors forward and reverse using four buttons:
    Button 1 is pressed  motor 1 runs in forward direction until button 1 is released
    Button 2 is pressed  motor 1 runs in reverse direction until button 2 is released
    Button 3 is pressed  motor 2 runs in forward direction until button 3 is released
    Button 4 is pressed  motor 2 runs in reverse direction until button 4 is released
    No button is pressed  no motor running
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 6: Lab2b: Forward and reverse of motor using buttons
There will be error flag reading from the Driver
      If there is Open Load flag, the Driver will not stop.
      If there is Over Current or Over Thermal flag, the Driver will stop.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 7: Lab2b: Forward and reverse of motor using buttons
We will also learn to read truth table and implement it in code
We will use FreeRTOS based code
Please refer to previous lab to set up the STM32CubeMX and STM32CubeIDE project
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 8: Lab2b: Forward and reverse of motor using buttons
Open STM32MCubeMX
Click
Click
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 9: Lab2b: Forward and reverse of motor using buttons
STM32CubeMX - STM32Cube initialization code generator - STMicroelectronics
    Caution!
    The .ioc file in the project uses STM32CubeMX version 6.12.1.
    If you have different type of version that older than this version, you will not be able to open it and you need to update it or to download the new installation from ST website
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 10: Lab2b: Forward and reverse of motor using buttons
For code with 1 button function, B1 (Blue Button) will be used
This code is used to check your Driver and Mirror’s motors connection
Set the MCU pins in STM32CubeMX as described.
  Four GPIO output pins
    PB15 for INA1
    PB1 for INA2
    PB13 for INB1
    PB14 for INB2
  Four external input pins for buttons
    PC13 (GPIO_EXTI13) for BUTTON (B1 or Blue Button)
  Two GPIO input pins for feedback LO1 and LO2
    PC6 for LO1
    PC5 for LO2
    Caution! These two pins MUST be connected to pull-up connection.
  PA5 is additionally set as TIM2_CH1 and can be used for debugging/testing purpose.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 11: Lab2b: Forward and reverse of motor using buttons
Set GPIO Mode and Configuration as below:
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 12: Lab2b: Forward and reverse of motor using buttons
Example: INA1 setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 13: Lab2b: Forward and reverse of motor using buttons
Example: LO1 setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 14: Lab2b: Forward and reverse of motor using buttons
Example: BUTTON setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 15: Lab2b: Forward and reverse of motor using buttons
Fill with 170 and it will find the solution automatically
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 16: Lab2b: Forward and reverse of motor using buttons
Check or set NVIC Mode and Configuration as below:
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 17: Lab2b: Forward and reverse of motor using buttons
Set SYS Mode and Configuration as below:
Select Timebase Source other than SysTick
for FreeRTOS based code
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 18: Lab2b: Forward and reverse of motor using buttons
Set FREERTOS Mode and Configuration as below:
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 19: Lab2b: Forward and reverse of motor using buttons
Truth table of INx1, INx2, and PWMx
Because we will not connect PWMx pins of the Driver board to NUCLEO pins, we will keep the level of PWMx to be HIGH (1)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 20: Lab2b: Forward and reverse of motor using buttons
Truth table of INx1, INx2, and PWMx
In this case, motor will run when one of INx pin level is HIGH and the other is LOW
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 21: Lab2b: Forward and reverse of motor using buttons
The code related to truth table
Forward
Reverse
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 22: Lab2b: Forward and reverse of motor using buttons
Implementation: in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 23: Lab2b: Forward and reverse of motor using buttons
To be noticed for LO1 and LO2
Truth table of LO1 and LO2
Compare these rows with the code of the next page
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 24: Lab2b: Forward and reverse of motor using buttons
Implementation: in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 25: Lab2b: Forward and reverse of motor using buttons
Button implementation, in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 26: Lab2b: Forward and reverse of motor using buttons
One button implementation, in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 27: Lab2b: Forward and reverse of motor using buttons
We can observe the variables in Live Expressions
Debugging
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 28: Lab2b: Forward and reverse of motor using buttons
Observe the behavior of mirror’s motors!
    First pressing  motor 1 runs in forward direction for 1s
    Second pressing  motor 1 runs in reverse direction for 1s
    Third pressing  motor 2 runs in forward direction for 1s
    Fourth pressing  motor 2 runs in reverse direction for 1s
    Another pressing will come back to first pressing, and so on
    No button is pressed  no motor running

## Slide 29: Lab2b: Forward and reverse of motor using buttons
For code with 4 buttons function
Set the MCU pins in STM32CubeMX as described.
  Four GPIO output pins
    PB15 for INA1
    PB1 for INA2
    PB13 for INB1
    PB14 for INB2
  Four external input pins for buttons
    PC10 (GPIO_EXTI10) for BUTTON1
    PC11 (GPIO_EXTI11) for BUTTON2
    PC12 (GPIO_EXTI12) for BUTTON3
    PD2 (GPIO_EXTI2) for BUTTON4
  Two GPIO input pins for feedback LO1 and LO2
    PC6 for LO1
    PC5 for LO2
    Caution! These two pins MUST be connected to pull-up connection.
  PA5 is additionally set as TIM2_CH1 and can be used for debugging/testing purpose.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 30: Lab2b: Forward and reverse of motor using buttons
Set GPIO Mode and Configuration as below:
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 31: Lab2b: Forward and reverse of motor using buttons
Example: INA1 setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 32: Lab2b: Forward and reverse of motor using buttons
Example: LO1 setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 33: Lab2b: Forward and reverse of motor using buttons
Example: BUTTON1 setting
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 34: Lab2b: Forward and reverse of motor using buttons
Check or set NVIC Mode and Configuration as below:
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 35: Lab2b: Forward and reverse of motor using buttons
Clock Configuration, SYS Mode and Configuration,
and FREERTOS Mode and Configuration
are the same with previous exercise
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 36: Lab2b: Forward and reverse of motor using buttons
Four (4) buttons implementation, in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 37: Lab2b: Forward and reverse of motor using buttons
With 4 buttons implementation, in main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 38: Lab2b: Forward and reverse of motor using buttons
Observe the behavior of mirror’s motors!
    Button 1 is pressed  motor 1 runs in forward direction until button 1 is released
    Button 2 is pressed  motor 1 runs in reverse direction until button 2 is released
    Button 3 is pressed  motor 2 runs in forward direction until button 3 is released
    Button 4 is pressed  motor 2 runs in reverse direction until button 4 is released
    No button is pressed  no motor running

## Slide 39
Thank you and good luck!